# Support for the design process

The following document serves as an aid during the design process. By observing the points below, the production costs can be reduced as much as possible.

### Existing machines at TELE Haase:

| Line 1 |  |  |
| --- | --- | --- |
| Stencil Printer |  | PCB-Length [mm] | PCB-Width [mm] | Height [mm] |  |
| Ersa Versaprint 2 Pro² | Min. | 50 | 50 | 0,5 |  |
|  | Max. | 345 | 250 | 4 |  |
| Pick and Place Machine |  | PCB-Length [mm] | PCB-Width [mm] | Height [mm] | Component size [mm] | Component height [mm] |
| Mimot Mit4 Speed | Min. | 50 | 50 | 0,5 | 01005 Bauteil |  |
|  | Max. | 345 | 250 | 4 | 14 x 14 | 25 |
|  |  | PCB-Length [mm] | PCB-Width [mm] | Height [mm] | Component size [mm] | Component height [mm] |
| Mimot MB200-21 | Min. | 50 | 50 | 0,5 | 01005 Bauteil |  |
|  | Max. | 345 | 250 | 4 | 55 x 55 | 10 |
| Reflow |  | PCB-Length [mm] | PCB-Width [mm] | Height [mm] | Component height [mm] |  |
| Ersa Hotflow 4/14 (N2) | Min. | 50 | 50 | 0,5 |  |  |
|  | Max. | 345 | 250 | 4 | 25 |  |

| Line 2 |  |  |
| --- | --- | --- |
| Stencil Printer |  | PCB-Length [mm] | PCB-Width [mm] | Height [mm] |  |
| Ersa Versaprint S1 | Min. | 50 | 50 | 0,5 |  |
|  | Max. | 345 | 350 | 4 |  |
| Pick and Place Machine |  | PCB-Length [mm] | PCB-Width [mm] | Height [mm] | Component size [mm] | Component height [mm] |
| Mimot MX | Min. | 50 | 50 | 0,5 | 01005 Bauteil |  |
|  | Max. | 345 | 350 | 4 | 12 x 12 | 25 |

| Reflow |  | PCB-Length [mm] | PCB-Width [mm] | Height [mm] | Component height [mm] |
| --- | --- | --- | --- | --- | --- |
| Hotflow 3/14 (N2) | Min. | 50 | 50 | 0,5 |  |
|  | Max. | 345 | 350 | 4 | 25 |
| AOI |  | PCB-Length [mm] | PCB-Width [mm] |  |  |
| Göpel OptiCon | Min. | 50 | 50 |  |  |
|  | Max. | 350 | 400 |  |  |
| Template washer |  |
| Kolb PS 300 |  |
| Drying storage cabinet |  |
| Super Dry TOTECH SD702 |  |
| Blank separation |  |
| Cab Maestro 4M |  |
| Wave soldering |  |
| Powerflow (N2) |  |

### Design guideline for the electronic manufacturing services by TELE:

| SMT/THT (Through Hole Technology) |
| --- |
| Component requirements: |
| Component size: | Max.: | 50 x 50 mm (bei 0,5 mm Pitch) |  |
|  | Max.: | 40 x 30 mm (bei 0,3 mm Pitch) |  |
| Component height: | Mimot Mit4 | max. 25 mm |  |
|  | Mimot MB200 | max. 10 mm |  |
|  | Mimot MX | max. 25 mm |  |
| Component packing: | Belt / Reel | Preferred |  |
|  | Tray | Rather for small batches |  |
|  | Rails | Only for small batches |  |
|  | Bulk material | Only for THT |  |

| Consider the preferred marking and orientation of the SMD components in the tape. |  |
| --- | --- |
| PCB requirements: |
| Altium: Usage of standardized outputjob-files |
| Files (ASCII – Format or excel in mm) Format: Placement position ¦ Component designation ¦ X-Coordiante ¦ Y-Coordinate ¦ Rotation |  |
| PCB panel data: Dimensions of total and single PCB panel |  |
| Automatically generated part list |  |
| Assembly plan |  |
| STEP-Files incl. 3D model of the complete device |  |
| Zipped dataset with Gerber and PCB panel data (for mask purchase order). |  |
| Enable overlaying of different print indices. |  |
| Schematics: |
| Clarity and readability for second (Inlets left, outlets right, ground below). Too many connecting lines replace by labeling. Mark the voltage level clearly. |  |
| Partnumbers of important/ unusual components can be supplemented in the schematics. |  |
| Cite the value, size and Refdes. of each components. |  |
| At e.g. N Prints / device is the following name for the Refdes.: 1xx / 2xx … Nxx |  |
| For connection points without use (for example controller), no label name needs to be assigned. |  |
| Requirements for the producibility of the Prints |
| PCB panel: | Min.: | 50 x 50 mm |  |
| Mimot Mit4 | Max.: | 345 x 250 mm |  |
| Mimot MB200 | Max.: | 345 x 250 mm |  |
| Mimot MX | Max.: | 345 x 350 mm |  |
| Thickness: | 0,5-2 mm | 1,6 mm preferred |  |
| Surface: | Chem. Zinn (Sn) | ≥ 1,0µ (standard) |  |
|  | Chem. Nickl-Gold (Ni-Au) | ≥ 0,15µ (standard) |  |
|  | Hot Air Leveling (HAL) | ≥ 1,0 µ ≤ 25 µ (in consultation) |  |
|  | Organic CU (OSP) | (in consultation) |  |
| 2 diagonally positioned fiducials (ideally asymmetrical to the print contour) per print side with SMD placement. |  |
| Test mark necessary. |  |
| Minimum distance Fiducial edge to components/ through-hole plating: 2mm |  |
| (( , # , + mögl.) IST: Cu=DM1,20; Lack=DM2,30 mm. See the following picture: |  |
| Concern CEM1: Additional centering holes due to linear expansion. |  |
| Additional marginal strips (5mm) are needed for the transport, so far not possible on print. |  |
| Origin: Preferably as a cross in a corner on the top of the print (no solder resist). For SMD placement also on the bottom side of the print (in this case the two originals must lie directly above one another). |  |
| If necessary, open area of 8 x 8 mm provided for 2D barcode labels. |  |
| PCB panel separation: Minimum distance of 0.5 mm between the conducting path or copper surface and the print outer contour. |  |
| Min. 1.5 mm distance from component outer edge to the scratch edge or 1 mm to the milled edge after consultation with PUS. |  |

| The residual strip height (depending on the PCB thickness) is shown in the following table and should be entered in the form “Data for PCB”. A PCB-Thickness [mm] B residual strip height [mm] Tol. [mm] 0,8 0,3 +/- 0,1 1 0,3 +/- 0,1 1,2 0,4 +/- 0,1 1,5 0,5 +/- 0,1 2,0 0,5 +/- 0,1 |  |
| --- | --- |
| Milled outer contour: Predetermined breaking holes must lie, as the following figure shows, around the drilling radius within the contour in order to minimize rework: |  |
| As a result of the different requirements by SMT and the print manufacturers discuss the solder resist cover of the Vias (Restring) on the surge side |  |
| For fine-pitch components, solder resist must be provided between the pads. |  |
| On the reflow site Vias should not lie inside of SMT-Pads. |  |
| Both-Sided Placement: |
| For cost reasons, this should be principally avoided. If it is necessary, there are 2 options: |
| Single-sided reflow (bottom wave soldering): The upper side will be reflow soldered and the bottom side bonded. In the next step the bottom side will be soldered by wave soldering. |
| Do not use components smaller than 0805 and Finepitch on the surger side. |  |
| Components with special Pad-Geometries should be used on the surger side. |  |
| Consider the direction of soldering (components should be positioned parallel to the shaft). |  |
| The higher the component, the more distance must be maintained to the next (shadowing). |  |
| Both-sided Reflow: |
| Small components of the PCB should rather be placed on the bottom side of the print. |  |
| In both cases: Min. 1.5 mm distance from component outer edge to the scratch edge or 1 mm to the milled edge after consultation with PUS. On the bottom side no components higher than 4 mm should be positioned. |  |

Reflow soldering profile:

By default, TELE Haase uses lead-free pastes.
Upon request leaded pastes can be used.

Wave soldering profile: